## Slide 1
Life Cycle Assessment - Practicum
Stefano Cucurachi, Leiden University, CML
©Leiden University, 2018

## Slide 2: Electricity from fuel oil
Notes: Remember the simple example we considered in the lecture?

## Slide 3: Electricity from fuel oil
Global warming
Acidification
Notes: We calculated for this system the impacts on global warming and acidification.

## Slide 4
Scaling factor: 2
Scaling factor: 100
Processes scaled
Notes: Here you see our scaled processes.

## Slide 5
Amount | Unit | Substance
100 | l | crude oil
120 | kg | CO2
14 | kg | SO2
Life cycle inventory (the flows to and from the environment
Notes: Our inventory (LCI) results

## Slide 6
Amount | Unit | Substance | Characteriz-ation factor | Unit | GW
100 | l | crude oil | - | kg-CO2-eq. | -
120 | kg | CO2 | 1 | kg-CO2-eq. | 120
14 | kg | SO2 | 0.1 | kg-CO2-eq. | 1.4
 |  |  |  | Total | 121.4
Amount | Unit | Substance | Characteriz-ation factor | Unit | Acidification
100 | l | crude oil | - | kg-SO2-eq. | -
120 | kg | CO2 | - | kg-SO2-eq. | -
14 | kg | SO2 | 1 | kg-SO2-eq. | 14
 |  |  |  | Total | 14
Global warming
Acidification
Life cycle inventory (the flows to and from the environment
Notes: And our impact scores (LCIA) results.

## Slide 7
Process tree/flow diagram: NdFeB magnets
Notes: What if we wanted to take into account a more realistic case study? Please take a look at the document provided in the word format. We want to conduct using excelm so no specific LCA software for now, the environmental impacts associated with producing NdFeB magnets.

## Slide 8
ndfebmagnet.net
Process tree/flow diagram: NdFeB magnets
Notes: I grabbed this from the web. What we see here is a schematic representation of the processes involved in producing neodymium magnets, from extraction of raw materials, to the manufacturing phases.

## Slide 9
Assembly
Energy B
Raw material D
Ancillary material A
Raw material C
Ancillary material F
Water
Compon-ent
B
Raw material E
Compon-ent A
Energy A
Disposal
Use
Suh, 2009
Process tree/flow diagram: system boundaries and cut-off
Notes: 9
9
Keep in mind that we want to keep this system manageable.

## Slide 10
Capital
Cut-off
Cut-off
Capital
Capital
Capital
Capital
Capital
Capital
Capital
Capital
Capital
Capital
Capital
Assembly
Energy B
Raw material D
Ancillary material A
Raw material C
Ancillary material F
Water
Compon-ent
B
Raw material E
Compon-ent A
Energy A
Disposal
Use
Suh, 2009
Notes: 10
10
If we keep on adding inputs and outputs, the system will expand.

## Slide 11
Suh, 2009
Notes: 11
11
And quite fast…

## Slide 12
Suh, 2009
Notes: 12
12
BOOM! Get out of control!

## Slide 13
Process tree/flow diagram: NdFeB magnets
Notes: 13
13
To avoid that, for this example, we made some modelling choices and simplified the system. All the data that is relevant for this system is available in the excel sheet that comes with the exercise.

## Slide 14
Process tree/flow diagram: NdFeB magnets
Notes: 14
14
This are the inputs and outputs of the system. Take a look at the description of the exercise and try and solve the system. Good luck.

## Slide 15
Scaled processes
Notes: 15
15

## Slide 16
Scaled processes
Notes: 16
16
To be shown after the exercise for students to compare their results.

## Slide 17: Impact Assessment

## Slide 18
Process tree/flow diagram: NdFeB magnets
Notes: 18
18
To be shown after the exercise for students to compare their results.

## Slide 19
What did we find?
Interpretation?
Demonstration in software
Discussion of results
Notes: Reflection points in class.

## Slide 20
Life Cycle Assessment - Practicum
Stefano Cucurachi, Leiden University, CML
©Leiden University, 2018

## Slide 21
Sustainable Management of Critical Raw Materials
www.suscritmat.eu